## Slide 1
AFFI
AI Flood Inundation Early Warning System
Physics-Guided AI for Real-Time Flood Forecasting in Semi-Arid Watersheds
Presented to: Pima County Flood Control District
Solman Raju Sarva | MSc — AI & Hydrology Researcher

## Slide 2
Agenda
What we will cover today
01
The Problem
Why rural Arizona flash floods are uniquely dangerous
02
Why Current Systems Fail
Gaps in NOAA, FEMA, Google Flood Hub
03
AFFI Solution Overview
6-stage physics-guided AI pipeline
04
Technical Deep Dive
Meteorology → Hydrology → Hydraulics → Alerts
05
Task 1 Completed
Forecast interface, MAP computation, alert logic validated
06
Roadmap: Tasks 2–6
LSTM, U-Net, Probabilistic Output, Benchmarking, Alert System
07
Results & Performance
360x faster than physics models; sub-60s pipeline
08
Why Pima County
Direct applicability to Pima County wash system
09
Timeline & Next Steps
Path from pilot to production

## Slide 3
The Problem: Flash Flooding in Rural Arizona
Deadliest natural hazard. Worst timing. No warning.
Human Cost
• 287 flood deaths in Arizona (2000–2023)
• More than tornadoes + hurricanes + earthquakes combined
• Most fatalities: drivers encounter flooded roadways
• Little or no advance warning available
• $180M annual property damage statewide
Pilot Watershed: Upper Sonoita Creek
• 143.6 km² semi-arid terrain, Santa Cruz County
• 12 major flood events since 1980
• 3 events exceeded 50-year return period
• SR-82 = only evacuation route for 3,200 residents
• 2006 monsoon: $12M damage, 340 displaced, route closed 72 hrs
• Emergency managers received NO advance inundation map
The Core Gap
• Physics flood models take 4–6 hours to run
• Arizona monsoon flash flood arrives in < 2 hours
• Warning comes AFTER the flood hits
• Time gap between warning and impact = lives lost
• Current systems designed for large, gauged rivers only
• Hundreds of ephemeral washes remain ungauged

## Slide 4
Why Current Systems Fail for Rural Arizona
Each excels at its purpose — none address our problem
NOAA NWM
• ✓ Streamflow forecasts up to 7 days
• ✗ Requires stream gauge calibration data
• ✗ Does not produce spatial flood maps
• ✗ Not designed for ephemeral channels
Google Flood Hub
• ✓ Global flood forecasting coverage
• ✗ No coverage for ungauged basins
• ✗ Limited to major rivers in AZ
• ✗ Partial real-time map capability
FEMA FIRM
• ✓ Static hazard zone maps
• ✗ No event-specific data
• ✗ Not real-time or storm-updated
• ✗ Reflects historical risk only
AFFI fills this gap: probabilistic inundation maps for ungauged rural arroyos with lead times sufficient for emergency action.

## Slide 5
AFFI Solution Overview
Physics-guided AI pipeline. Speed + Accuracy + Uncertainty quantification.
< 60 seconds
Pipeline Run Time
360×
Faster than HEC-RAS
31
Ensemble Members
< 80 hrs
Per Watershed Deployment
The Six-Stage Physics-Based Pipeline
Stage 1 Meteorology
• GFS/HRRR Ensemble
→
Stage 2 Hydrology
• LSTM Model
→
Stage 3 Hydraulics
• U-Net Surrogate
→
Stage 4 Probabilistic
• 31 Ensemble Maps
→
Stage 5 Benchmarking
• Return Period Analysis
→
Stage 6 Alert System
• JSON Alert Packet

## Slide 6
Architecture Deep Dive: Stages 1–3
Physics-based forecast → AI hydrology → AI hydraulics
Stage 1: Meteorology (~5 sec)
• Ingests GFS ensemble (31 members, 6-hourly updates)
• Also HREF ensemble (~10 members, hourly, CONUS)
• Computes Mean Areal Precipitation (MAP) over watershed
• Accumulation windows: 1h to 168h
• NOT AI — physics-based numerical weather prediction from NOAA
• MAP = spatially averaged rainfall (critical for accuracy)
Stage 2: Hydrology / LSTM (~8 sec)
• Converts MAP → streamflow hydrograph (ft³/s)
• LSTM captures temporal dependencies in rainfall-runoff
• Base training: Walnut Gulch 70-year record
• Fine-tuning: target watershed with final layers only
• Needs as few as 10–15 years of local data
• Incorporates slope, soil, vegetation, elevation
• NSE > 0.80 validated on 531 US watersheds
Stage 3: Hydraulics / U-Net (~45 sec)
• Converts discharge → spatial flood inundation map
• Trained on 250 physics-based HEC-RAS simulations
• U-Net takes 2D input (terrain + discharge), outputs 2D flood depth
• Physics constraints enforced:
• • Gravity: water never flows uphill
• • Monotonicity: higher discharge = greater inundation
• • Mass conservation: runoff ≤ rainfall volume

## Slide 7
Architecture Deep Dive: Stages 4–6
Probabilistic output → Benchmarking → Operational alerts
Stage 4: Probabilistic Output (~2 sec)
• Full pipeline for all 31 GFS ensemble members
• Produces 31 flood maps per forecast event
• Output products:
• • Median flood map (best estimate)
• • 90th percentile (worst-case, 10% exceedance)
• • Probability map: P(depth > 0.5m) per pixel
• • Uncertainty map: std dev across all 31 members
Stage 5: Benchmarking (~1 sec)
• Compares predictions to federal engineering standards
• NOAA Atlas 14 precipitation frequency data
• USGS regional regression peak discharge
• Classifies each event by return period:
• • 2-year → routine maintenance storm
• • 10-year → design storm standard
• • 50–100 year → major emergency response
Stage 6: Alert System (~1 sec)
• Integrates all pipeline components into operational alert
• Alert levels: ADVISORY / WATCH / WARNING
• Driven by probability of exceedance (PoE):
• • Advisory: ≥ 25% PoE
• • Watch: ≥ 50% PoE
• • Warning: ≥ 70% PoE
• RESTful API (FastAPI) for government integration
• EOC-ready dashboard, auto-updates every 6 hours

## Slide 8
Lead Time → Confidence Framework
Confidence increases as storm approaches. Right data, right time.
2 – 7 Days
• GFS Ensemble (31 members)
• Low – Medium
• • Pre-position resources • Early briefings to leadership • Equipment staging plans
6 – 24 Hours
• HRRR + Updated GFS
• Medium – High
• • Road closure decisions • Evacuation planning • Staff on-call notifications
0 – 6 Hours
• MRMS Radar + Nowcast
• High
• • Active road closures • Emergency response dispatch • Public warnings issued
Key: Confidence scales from LOW (far forecast) to HIGH (imminent). Action scales accordingly.

## Slide 9
Task 1: Completed & Validated
Meteorological Forecast Interface — Production-ready as of May 2026
Deliverables Produced
• D1.1: GFS ensemble forecast ingestion via Open-Meteo API
• D1.2: 5-point grid for Upper Sonoita Creek watershed
• D1.3: Mean Areal Precipitation (MAP) computation engine
• D1.4: Alert threshold logic benchmarked vs NOAA Atlas 14
•
• Output files:
• • task1_alert_packet.json — structured forecast data
• • task1_forecast_dashboard.png — visualization
• • Interactive dashboard (HTML) — 4-panel Plotly charts
• • SQLite database — persistent alert history
Validation & Testing
• ✓ Alert thresholds calibrated for Sonoita Creek:
• Advisory: 0.25" (1hr) / 0.75" (24hr)
• Watch: 0.50" (1hr) / 1.25" (24hr)
• Warning: 1.00" (1hr) / 2.00" (24hr)
•
• ✓ Dummy rainfall stress test passed
• All return periods validated (2–100 year)
• Each scenario triggers correct alert level
•
• ✓ 30 automated unit/integration tests pass
• ✓ Code review completed with findings documented
Task 1: PRODUCTION-READY — Pipeline operational and validated

## Slide 10
Task 2: Physics-Guided LSTM Hydrology Model
Teaching AI how desert floods work — Transfer learning approach
Two-Stage Training Strategy
• Stage 1 — Base Training:
• Train on Walnut Gulch (70-year record)
• Learns desert hydrology fundamentals:
• • Rapid infiltration patterns
• • Hortonian overland flow
• • Ephemeral channel routing
•
• Stage 2 — Fine-Tuning:
• Adapt model to target watershed
• Only final layers updated
• Needs only 10–15 years local data
Why LSTM is the Right Choice
• • Captures temporal dependencies in rainfall-runoff
• • Today soil moisture depends on yesterday rainfall
• • Validated on 531 US watersheds (Kratzert et al., 2019)
• • Nash-Sutcliffe Efficiency (NSE) > 0.80
• • Matches or exceeds calibrated physics models
• • Uses watershed attributes: slope, soil, vegetation, elevation
Deliverables (Planned)
• D2.1: Walnut Gulch "Anchor" + Sonoita "Pilot" models
• D2.2: Performance scorecard (NSE, Peak Timing)
• D2.3: Training config files — reproducible experiments
• D2.4: Validation plots — AI vs historical floods
• D2.5: Deployment checklist for new watersheds
•
• Benchmarking against 2014 Hurricane Odile remnants.
• Return period discharge estimation (Q2–Q100).

## Slide 11
Task 3: U-Net Hydraulic Surrogate Model
Converting predicted discharge into spatial flood inundation maps
HEC-RAS Training Data
• • 250 HEC-RAS simulations (10 discharge levels × 5 replicates)
• • Discharge levels: Q2, Q5, Q10, Q25, Q50, Q100 + intermediates
• • Manning’s n variation for roughness uncertainty
• • Calibrated against 2006 Santa Cruz monsoon flood
• • 1-meter lidar DEM from USGS 3DEP
•
• U-Net learns the physics — not just patterns.
U-Net Architecture (ResUNet)
• • Input: DEM + slope + channel distance + discharge
• • Output: flood depth raster (feet)
• • 4 encoder/decoder levels with skip connections
• • Adam optimizer, combined MSE + SSIM loss
•
• Validation targets:
• • IoU > 0.75 on held-out watersheds
• • Critical Success Index (CSI) comparison
Physics Constraints Enforced
• 1. Gravity Constraint:
• Water depth = 0 for pixels above water surface elevation
•
• 2. Monotonicity Constraint:
• Higher discharge → equal or greater flood extent
•
• 3. Mass Conservation:
• Total runoff volume ≤ total rainfall volume
•
• Ensures physical plausibility outside training distribution.

## Slide 12
Tasks 4–6: From Prediction to Operational Alert
Probabilistic products → Benchmarking → EOC-ready dashboard
Task 4: Probabilistic Risk Products
• • Full pipeline executed for all 31 ensemble members
• • Median, 90th percentile, probability, uncertainty rasters
• • Time-to-peak estimate per ensemble member
• • EOC dashboard: 6-panel visualization
•
• Primary decision product:
• P(flood depth > 0.5m) = [0–100%] per pixel
Task 5: Benchmarking & Validation
• • Compare predictions to NOAA Atlas 14 + USGS standards
• • Return period classification (2yr – 100yr)
• • Validate on 5 historical AZ flood events:
• 1983, 1993, 2006, 2014, 2017
• • Sensitivity analysis: input uncertainty propagation
Task 6: Operational Alert System
• • Alert Logic Specification signed off by local OEM
• • RESTful API (FastAPI) with key authentication
• • EOC Dashboard: Streamlit/Dash application
• • Auto-updates every 6 hours with new GFS data
• • Operational testing during monsoon season

## Slide 13
Performance: AFFI vs. Current Systems
Numbers that matter for emergency decision-making
Metric
Current (HEC-RAS)
AFFI
Improvement
Time to flood map
4–6 hours
< 60 seconds
360× faster
Watersheds covered
~12% (gauged only)
Any watershed
Statewide
Forecast lead time
0–2 hours
Up to 7 days
84× longer
Ensemble members
1 (deterministic)
31 (probabilistic)
Uncertainty quantified
Cost per forecast
~$2,400 (EOC act.)
~$0.04 (cloud)
60,000× cheaper
Ungauged basins
Requires gauge cal.
Any watershed
Ungauged-ready

## Slide 14
Validation Plan & Performance Targets
Four independent benchmarks — all from peer-reviewed literature
In-Sample Accuracy
• LSTM on held-out years (2001–2006, 20 watersheds)
• Target: NSE > 0.75 KGE > 0.70
• Ref: Moriasi et al. 2007
Out-of-Sample Generalization
• LSTM on 5 held-out watersheds (never seen)
• Target: NSE > 0.65
• Ref: Kratzert et al. 2019
Historical Event Validation
• Full pipeline on 5 major AZ flood events
• Target: IoU > 0.75 vs post-event surveys
• Ref: FEMA disaster assessments
Speed Benchmark
• Wall-clock: GFS input to flood map
• Target: < 60 seconds
• Ref: Flash flood warning req.
Baselines: Simple LSTM (no attributes) • HEC-HMS+HEC-RAS (physics) • FEMA static FIRM maps

## Slide 15
Transferability: From Pilot to Any Watershed
40–80 hours per new watershed — not a full rebuild
How Transferability Works
• Every AFFI component designed for transfer from day one.
•
• Per-watershed inputs that change:
• • AOI / Bounding Box — 1 hour (USGS National Map)
• • NOAA Atlas 14 Benchmarks — 2 hours
• • Alert Thresholds — 4 hours (County OEM + NOAA)
• • 1m DEM terrain data — 4 hours (USGS 3DEP)
• • HEC-RAS model — 20–40 hours
• • LSTM fine-tuning — 8 hours (if gauge data exists)
• • U-Net re-training — 10 hours
•
• Architecture, alert logic, API, dashboard — unchanged.
Statewide Expansion Strategy
• Step 1: Prioritize AZ watersheds by:
• • USGS 3DEP 1m lidar availability
• • Flash flood risk to populated areas
• • No existing operational flood warning
•
• Step 2: Rapid deployment (40–80 hrs/watershed)
•
• Step 3: Cross-watershed validation test
•
• Step 4: Statewide dashboard — all watersheds on one map
•
• All data sources FREE from federal agencies.

## Slide 16
Why This Matters for Pima County Flood Control
Same semi-arid flash flood challenge — with higher stakes
Pima County Context
• • One of fastest-growing counties in the US
• • Hundreds of ephemeral washes and arroyos
• • Tucson metro area in flood-prone region
• • Monsoon season: July–September heavy rainfall
• • Time of concentration as short as 15–30 minutes
• • Channels dry 300+ days/yr, catastrophic flows in minutes
• • Climate: 15–40% more extreme precipitation by 2050
What AFFI Delivers Pima County
• • Sub-60-second flood maps for ANY wash/creek
• • 7-day forecast lead time (up to 84x current)
• • Probabilistic output — know your confidence level
• • No stream gauge needed — ungauged basins
• • All data FREE (NOAA, USGS, USDA)
• • Cloud compute cost: ~$0.04 per forecast run
• • EOC dashboard ready for County Emergency Ops
Immediate ROI
• Current approach:
• • Reactive response to flash floods
• • EOC activation: $2,400/hour
• • Post-flood debris: $180K–$450K per event
• • Bridge/road repair: $1.2M–$8M per segment
•
• With AFFI:
• • Proactive: know BEFORE flood hits
• • Pre-position resources strategically
• • Close roads with confidence (not guesswork)
• • Protect 1.8M+ Pima County residents

## Slide 17
Data Sources & Technology Stack
All data from federal agencies at zero licensing cost
Data Type
Source
Streamflow (anchor)
USDA ARS — Walnut Gulch
Streamflow (pilot)
USGS NWIS — Gauge 09481740
Terrain (DEM)
USGS 3DEP — 1m lidar
Forecast data
NOAA GFS — 31 ensemble members
High-res forecast
NOAA HRRR — 18 ensemble members
Radar rainfall
NOAA MRMS — 1km resolution
Soil data
USDA SSURGO — 1:24,000
Land cover
USGS NLCD — 30m
Watershed attributes
USGS GAGES-II — 9,322 watersheds
Flood benchmarks
NOAA Atlas 14 — all AZ counties
• Python 3.12 • pandas, numpy, scikit-learn • PyTorch (LSTM + U-Net)
• Plotly (dashboards) • Folium (map visualization) • FastAPI (REST API)
• SQLite (persistence) • YAML configs • 30 automated tests

## Slide 18
Timeline & Milestones
From current state to full operational deployment
COMPLETE
• Task 1: Meteorological Forecast Interface
• • GFS ensemble ingestion + MAP computation
• • Alert logic calibrated & validated
• • Interactive dashboard operational
→
PHASE 2 (NEXT)
• Task 2: LSTM Hydrology (base → fine-tune)
• Task 3: U-Net Hydraulic (train on HEC-RAS)
• Target: NSE > 0.75 in-sample, IoU > 0.75
→
PHASE 3
• Task 4: Probabilistic Risk Products
• Task 5: Benchmarking & Historical Validation
• Task 6: Alert System + EOC Dashboard
→
PHASE 4 (LAUNCH)
• Live testing during monsoon season
• Deploy to multiple Pima County washes
• Statewide dashboard all watersheds

## Slide 19
Thank You
Ready to pilot AFFI in Pima County
Let’s discuss how we can work together to protect Pima County communities.
Solman Raju Sarva | MSc — AI & Hydrology Researcher
University of Arizona — Hydrology Program

## Slide 20
Appendix: Detailed System Comparison
Why each existing system cannot serve rural Arizona flash floods
System | Forecast Type | Lead Time | Ungauged | Rural Arroyos | Real-Time
AFFI (Proposed) | Probabilistic inundation maps | Up to 7 days | Yes | Yes | Yes
NOAA NWM | Streamflow forecast | Up to 7 days | Limited | No | No
Google Flood Hub | Flood forecast + maps | Up to 7 days | No | No | Partial
FEMA FIRM | Static hazard zones | None (static) | Partial | Partial | No
First Street Found. | Property-level risk scoring | None (static) | Partial | No | No
FLASH System | Short-lead flash flood alerts | Hours to 1 day | No | No | Partial